## Slide 1: Explaining the variation of X/Y charge sharing of the SBS GEMs readout boards
Kondo Gnanvo

## Slide 3
COMPASS Readout Board
Pitch = 400 mm
Top strips width = 50 mm
Bottom strip width = 340 ~ 350mm
Kapton layer thickness = 50 mm
  Width at the top = 80 mm
  Width at the base should not be too much bigger than 80 um
Microscope view of the COMPASS readout

## Slide 4: JLab-SBS readout board (COMPASS-like)
Bottom strips
330 mm
Pitch
400 mm
Pitch
400 mm
Top strips
80 mm
~ 160 mm
Kapton Spread
at the base
Microscope view of the SBS readout at CERN

## Slide 5
Bottom strips
330 mm
Pitch
400 mm
Pitch
400 mm
Top strips
80 mm
160 mm
Kapton Spread
at the bottom
Consequences of the low quality readout production
Kapton spread
   bottom strip effective width is smaller than 350 mm
  Charge sharing top / Bot strips > 1
  Not critical if ratio not to high
Kapton spread  dielectric charging up
  local modification of the electric field
  bottom strip collect even less charges
  Charge ratio increases with the rate
  very critical at SBS rate level
Consequences of poor quality SBS Readout board

## Slide 6
Beam:
25 GeV Hadrons
5k particles/s
Size: 2 cm x 10 cm
X / Y = 1.81
Cosmic data
X / Y = 1.34
Beam:
120 GeV Protons
5k particles/s
Size: 1 cm x 2 cm
X / Y = 2.24
Big variation of the charge sharing fat different rate
poor production quality of SBS readout board

## Slide 7
Readout board quality for the future
@ CERN
  Pay more attention during production to the quality of the R/O board
  Reduce the kapton layer width to 90 micron (maximum)
In our detector lab @ UVa
  Acquire a microscope to check the R/O when we receive it from CERN
  Set up a test bench to measure the noise distribution of the R/Os before assembly
  Want to be able to test in a high rate environment the next chamber we are going to build against the current prototype.
  Is there anyone interested in another test beam at FNAL in the coming 2-4 months?